## Slide 1: Comparing Direct and Indirect Encoding for FPGA Bitstream Evolution
Thomas Bioren

## Slide 2: Presentation Outline
Relevant Background
  What is an FPGA?
  iCE40 FPGA Specifics
  What is Bitstream Evolution?
Why is this Important?
Methods
  Direct Encoding
  Indirect Encoding
Thesis Statement
Current Progress

## Slide 3: Relevant Background

## Slide 4: What is an FPGA?

## Slide 5: Field-Programmable Gate Array (FPGA)
An integrated circuit that can be repeatedly reprogrammed after manufacturing
Mimics logic gates with lookup tables (LUTs)
LUTs are connected together to form circuits
Use Cases:
  Prototyping circuits before mass-production
  Digital signal processing (DSP)
  Telecommunications
  Radar
  UAVs
Notes: https://www.ibm.com/think/topics/field-programmable-gate-arrays

## Slide 6: Programming an FPGA
Configured using a bitstream
Hardware design languages (HDLs) are compiled to bitstreams
Tools like Quartus can help design FPGAs

## Slide 7: iCE40 FPGA

## Slide 8: iCE40 FPGA
1,000 LUTs organized in logic tiles (pink)
LUTs are connected by nets to make a circuit

## Slide 9: Connectivity
LUTs have 4 inputs and 1 output
You cannot directly wire LUT I/O together
Nets (simplified)
  A grid of wires across the entire FPGA
  You tell a LUTs to connect to a specific net
Accelerating convolutional neural networks: Exploring FPGA-based architectures and challenges - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/The-structure-of-an-FPGA-11_fig5_381808932 [accessed 28 Oct 2025]

## Slide 10: Bitstream ASC File
Text file that represents the binary bitstream
Free to modify the file in any way
Majority of ASC configurations are detrimental or invalid
~ possible combinations of LUT configs alone in the FPGA

## Slide 11: Bitstream Evolution

## Slide 12: Bitstream Evolution
Using evolutionary algorithms to evolve a bitstream for a certain goal
Examples
  Tone Discrimination (pictured)
  Signal Generation
  Variance Maximization

## Slide 13: Why is this Important?

## Slide 14: Adaptive Systems
Systems that need to be fault-tolerant
Systems that need to adapt to rapidly changing environments
Deep-space probes, UAVs, etc.
Robots that adapt to their environment

## Slide 15: Neural Networks
Energy efficient
Allow reconfiguration for training
Notes: Johnston SP, Prasad G, Maguire L, McGinnity TM. An FPGA hardware/software co-design towards evolvable spiking neural networks for robotics application. Int J Neural Syst. 2010 Dec;20(6):447-61. doi: 10.1142/S0129065710002541. PMID: 21117269.

## Slide 16: Methods

## Slide 17: Direct FPGA Encoding Method

## Slide 18: Procedure
Python ASC Representation of Population
ASC Files
Upload to FPGA
Evaluate Bitstream's Fitness against Goal
Identify Best Individuals and Generate New Population
Directly modifying bitstream
All mutations (within mutation area) are fair game
Most mutations are bad
Some may damage the FPGA

## Slide 19: General Experiment Progression

## Slide 20: Indirect FPGA Encoding Method

## Slide 21: Procedure
Genotype Representation
Verilog Representation
Intermediate BLIF Representation (Yosys)
ASC File (nextpnr)
Upload to FPGA
Evaluate Fitness
Identify Best Individuals and Generate New Population
Using Cartesian Genetic Programming (CGP)

## Slide 22: Genotype Representation
Every individual is represented by an array of 32-bit integers
Each integer encodes LUT behavior and connections
Makes invalid configurations (almost) impossible
0000000000000000 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
LUT Behavior | Input 0 X offset | Input 0 Y offset | Input 1 X offset | Input 1 Y offset | Input 2 X offset | Input 2 Y offset | Input 3 X offset | Input 3 Y offset

## Slide 23: Thesis Statement
My goal is to prove bitstream evolution using an indirect encoding method yields a statistically significant increase in the average rate of fitness improvements per generation over direct encoding methods.

## Slide 24: Current Progress

## Slide 25: Experiment 1: Simulation
Beginning simulation now
Simple “proof of concept”
Faster evaluation
Timing is not guaranteed
  Digital logic only
Goal: Evolve a circuit that evaluates
Fitness Function: